EDM DrillMate

20i

Manual

1. Specifications ------------------------ 1

2. Installation--------------------------- 4

3. Control Panel------------------------ 6

4. Preparation-------------------------- 9

5. Discharge --------------------------- 10

6. Maintaining------------------------ 11

7. Parameters------------------------16

1. Specification

| Work table size | 550×360 mm |
| --- | --- |
| X travel | 350mm |
| Y travel | 250mm |
| W travel | 300mm |
| Z travel | 380mm |
| Max workpiece weight | 350kg |
| Hole Diameter | φ0.15-3.0mm |
| Distance from table to bottom of guide | 100～400 |
| Outside dimensions | 1000×1100×2100mm |
| Work Area | 1500×1400mm |
| Total weight | 350Kg |
| Power input | 3KVA |
| Input voltage | 415V 3P 50Hz |
| Max current | 30A |
| Current setting | 9 steps |
| Pulse setting | 9 steps |
| Fluid capacity | 25L |
| Max pressure | 70kg/cm2 |

Fig-1

2.Installation

Fig-2

The machine should be placed in a clean temperature controlled environment. (Dust Free)

Fig-3

3. Control panel

Fig—4

1.  Display				Display XYZ Coordinates and EDM Settings

2.  Power On				Power On Button

3.  Emergency Stop		E Stop Switch – Power Off or Emergency Cut Off Power

(Rotate Right to Restart Machine)

4.  Voltmeter				Show High Frequency Voltage and Crash Protection Voltage

(When Powered On – Should be about 10V

5.  T On Set				Change Power On Time / Control Drilling Speed

6.  T Off Set				Change Power Off Time / Control Chip Removal

7.	IP Set				Control Electric Current

8.  Sensitivity			Improve Steadiness

9.  Water Pump Switch		Start and Close High Pressure Water Pump

10. High Frequency Switch	High Frequency Power On, Open Spindle (16), Make Electrode

Tube Rotate (70 rpm) – Ready to Drill

11. Z Pause Switch			If T T are both off, Z Drilling Pauses, If T on, Z continues to drill.  						If T T are both on, Z Automatically goes to the top.

12. Z Up and Down			Z Rapid Up and Down

13. Electrode Alignment		Press, adjust (15) to make Z travel up or down. (when electrode

touches work piece, Spindle stop and alarm, Use for Z Zero Clearing

function.

14. Electrode Repair Switch	Use to change discharge polarity, when drilling not steady or if

drilling deep hole.  (High electrode wear)

15. Voltage Set		To change discharge voltage (15V – 80V) Effects steadiness and

Speed.

16. Spindle Rotate Switch	Start and Stop Spindle Rotate (against clockwise direction)

17. W Axis Switch		W Axis up and down

18. W Axis Lock		Must be locked for transport

When the back door is opened the door switch turns off and all the electric control power of the machine is off.  Open the door and pull out the switch, the control system gets the power, everything goes on.

4. Preparation

4.1 Machining fluid.

Tap Water

4.2 Workpiece electrode

Workpiece is one of the electrodes; discharge line should be connected with the block tightly. The surface of the block should be clean.

4.3 Electrode guide

According to the size of the electrode pipe, select suitable guide.

4.4 Installation of electrode pipe.

See fig-5

Fig-5

Attention: for thinner electrode pipe, handling it carefully.

4.5  Electrode Tube

Electrode tubes should be high quality and should be straight.  Bent or curved electrodes will not EDM successfully.

- . Discharge drilling

  - Preparing for drilling

- Electrode is tightened by collet or chuck.

- Electrode tube is straight.

- If the pump pressure is within 5－6MPa .

  - Discharge step

- Moving X and Y-axis to the position of drilling.

- Moving the ram down until the bottom of the guide is 1～5mm high above the work piece.

- Follow recommended parameters putting “ON” “OFF” “IP””SV” in right way.

- Press the pump switch.

- Press the rotating switch.

- Press the pulse power switch.

- Adjusting servo resistor to control the voltage of the gap.

- When the tube is through the workpiece, drilling process of one hole is over. Press the up switch until pipe is above the hole. Moving the cross table for the next hole.

  - Display center

Please see the digital display manual.

###### 6. Maintaining

6.1 Pump

High-pressure pump is one of the important parts of the machine. It must be maintained properly.

Attention: lubricant oil should be on oil line, not higher or lower .The oil should be exchanged in 3 months.

6.2 Filter system

The filter core should be changed if the output pressure of water is unstable.

Fig-6

6.3 Rotating device

Drawing of rotating device is shown as fig-7.

Fig-7

If there is too much resistance on rotation, it may be caused by “○”type rubber or bearing, when the “○” type rubber is damaged. If water leaked into the bearing, the bearing will not function properly.  Change “○” type rubber and bearings.

See:fig-8

fig-8

The electric brushes should be exchanged when conducting

Power    See fig-9.

Fig-9

6.4 Generator

  - Electric control system.

The drawing of electric system is shown as fig-10.

Fig-10

  - Pulse power supply.

The drawing of pulse power supply is shown as fig-11.

Pulse power supply is generated by AP1 pcb. If coming into being on the discharge gap. It may be caused by damage of one of the transistors IRF250 replacing it.

  - Servo system

Servo system is depend of AP3 pcb. If there is something wrong on servo system. It may be caused by limit switches, the fuse on AP3 pcb. See Fig-11.

##### Fig-11

  - Depth control

Depth control is used in controlling the depth of cavity hole The usage of the depth control is in the display manual.

If a through hole is drilled, depth control is also set automatically. Please set the depth wear enough in accordance with the workpiece thickness and pipe wear.

Recommended Parameters

| WORK PIECE: Carbide ELECTRODE: Copper |
| --- |
| Electrode (mm) | Pulse On(Ton) | Pulse Off(Toff) | Current(Ip) | SV Sensitive | GAP voltage |
| Φ 0.2 | 1 | 2 | 1 | 0 | 30 — 50 |
|  | 1 | 3 | 1 | 1 | 25 — 45 |
| Φ 0.3 | 2 | 3 | 2 | 0 | 25 — 45 |
|  | 2 | 2 | 2 | 2 | 20 — 35 |
| Φ 0.5 | 2 | 2 | 3 | 3 | 25 — 35 |
|  | 3 | 2 | 3 | 2 | 30 — 40 |
| Φ 0.8 | 3 | 3 | 4 | 4 | 30 — 40 |
|  | 4 | 2 | 4 | 5 | 20 — 35 |
| Φ 1.0 | 4 | 2 | 4 | 4 | 25 — 40 |
|  | 4 | 3 | 5 | 6 | 20 — 35 |
| Φ 1.5 | 5 | 3 | 5 | 5 | 25 — 40 |
|  | 5 | 4 | 6 | 6 | 20 — 35 |
| Φ 2.0 | 6 | 3 | 6 | 7 | 20 — 30 |
|  | 6 | 4 | 7 | 8 | 20 — 30 |
| Φ 2.5 | 6 | 3 | 7 | 8 | 20 — 30 |
|  | 7 | 2 | 7 | 8 | 20 — 30 |
| Φ 3.0 | 7 | 2 | 8 | 8 | 20 — 30 |
|  | 7 | 3 | 9 | 9 | 20 — 30 |

All the parameters are for reference

Hint: More pulse width, more efficiency, more gap.

More pulse off, less efficiency, more stable.

More current, more stable, fast but more wear.

More SV sensitive, will work fast and stable.

Recommended Parameters

| WORK PIECE: Stainless Steel ELECTRODE: Brass |
| --- |
| Electrode (mm) | Pulse On(Ton) | Pulse Off(Toff) | Current(Ip) | SV Sensitive | GAP voltage |
| Φ 0.2 | 1 | 3 | 1 | 0 | 30 — 50 |
|  | 1 | 4 | 1 | 1 | 30 — 45 |
| Φ 0.3 | 2 | 1 | 1 | 1 | 30 — 50 |
|  | 2 | 3 | 2 | 3 | 25 — 45 |
| Φ 0.5 | 3 | 2 | 3 | 2 | 30 — 45 |
|  | 3 | 3 | 4 | 4 | 25 — 40 |
| Φ 0.8 | 5 | 2 | 3 | 4 | 25 — 40 |
|  | 4 | 3 | 4 | 5 | 20 — 35 |
| Φ 1.0 | 5 | 2 | 4 | 5 | 25 — 40 |
|  | 4 | 3 | 5 | 6 | 20 — 35 |
| Φ 1.5 | 6 | 2 | 5 | 6 | 20 — 35 |
|  | 5 | 3 | 6 | 7 | 25 — 40 |
| Φ 2.0 | 7 | 3 | 6 | 7 | 20 — 35 |
|  | 6 | 3 | 7 | 8 | 25 — 40 |
| Φ 2.5 | 7 | 3 | 7 | 8 | 25 — 35 |
|  | 8 | 2 | 7 | 7 | 25 — 30 |
| Φ 3.0 | 8 | 2 | 7 | 8 | 25 — 35 |
|  | 8 | 3 | 9 | 9 | 25 — 30 |

All the parameters are for reference

Hint: More pulse width, more efficiency, more gap.

More pulse off, less efficiency, more stable.

More current, more stable, fast but more wear.

More SV sensitive, will work fast and stable.

Recommended Parameters

| WORK PIECE: Copper or Brass ELECTRODE: Copper |
| --- |
| Electrode (mm) | Pulse On(Ton) | Pulse Off(Toff) | Current(Ip) | SV Sensitive | GAP voltage |
| Φ 0.2 | 1 | 2 | 1 | 0 | 30 — 50 |
|  | 1 | 3 | 1 | 1 | 20 — 45 |
| Φ 0.3 | 1 | 4 | 3 | 0 | 25 — 45 |
|  | 2 | 5 | 3 | 2 | 20 — 35 |
| Φ 0.5 | 3 | 3 | 4 | 3 | 25 — 35 |
|  | 3 | 2 | 3 | 2 | 30 — 40 |
| Φ 0.8 | 4 | 4 | 5 | 4 | 30 — 40 |
|  | 4 | 2 | 4 | 5 | 20 — 35 |
| Φ 1.0 | 4 | 3 | 5 | 4 | 25 — 40 |
|  | 5 | 4 | 5 | 6 | 20 — 35 |
| Φ 1.5 | 5 | 3 | 6 | 5 | 25 — 40 |
|  | 6 | 4 | 6 | 6 | 20 — 35 |
| Φ 2.0 | 6 | 3 | 7 | 7 | 20 — 30 |
|  | 7 | 2 | 7 | 8 | 20 — 30 |
| Φ 2.5 | 8 | 2 | 7 | 7 | 20 — 30 |
|  | 7 | 3 | 8 | 8 | 20 — 30 |
| Φ 3.0 | 8 | 2 | 7 | 8 | 20 — 30 |
|  | 8 | 3 | 9 | 9 | 20 — 30 |

All the parameters are for reference

Hint: More pulse width, more efficiency, more gap.

More pulse off, less efficiency, more stable.

More current, more stable, fast but more wear.

More SV sensitive, will work fast and stable.